## Slide 1: PAINT DRUM TESTING
industrial client: AKZO Nobel
By
Group 5
Bala Vignesh Subramanian- Project Manager
Prasad Pandeti – Communication Lead
Akanle Olusola Matthew – Project Team Member
Anand Kumar Kolakaluri- Project Team Member
Guided by
Academic Supervisor
Dr. Yolanda Sanchez Vicente.

## Slide 2: OBJECTIVES
Easy loading and unloading
Hydrodynamic & Buoyance properties
Design improvement & recommendations
Modelling and simulation
Creating prototype

## Slide 3: KEY MILESTONES:
Key objectives | Delivered
Corrosion of Nuts and Bolts | New Design
Reducing number of fittings | Thread Locking System
Buoyance &Hydrodynamic Properties | Increase in Weight
Finalising the material | Good buoyance properties
Marine Bio-fouling | Remedies for Bio-fouling
Analysis | Simulation for Thread Locking design

## Slide 4: CRITICAL PATH
Identifying the issues based on the Probability of risk
Key tasks are performed and delivered in mentioned time.

## Slide 5: RISK IDENTIFICATION
RISK IDENTIFICATION | RISK MITIGATION
Unknown of Buoyance properties of existing design | Calculating Buoyance using the dimensions of the clients drawing
Buoyance issues in the acrylic | Mitigating buoyance issues by reducing the hollow space inside the drum
3D Printing for Acrylic material | 
Max Temp of Acrylic material is 80 C | Keeping the print between 50 to 80 C
Locking issues in New design | Implementing Allen key type locking

## Slide 6: DESIGN

## Slide 7: 3-D VIEW OF THREAD LOCKING SYSTEM:
Picture1: Top Part
Picture 2: Bottom Part

## Slide 8: ASSEMBLY VIEW
Picture 3: Assembly View
Picture 4: Assembly View2

## Slide 9: SIMULATION

## Slide 10: STRUCTURAL ANALYSIS
Input:
Rotational Speed – 750rpm
Immersed Depth – 1m Young’s Modulus – 2.5 e^9 Pa Yield Strength – 2.86 e^7 Pa
Tensile Strength – 6 e^7 Pa
Temperature – 22 Degree Gravity – 9.8 m/sec2

## Slide 11: STRESS CALCULATION
Result:
Max Stress – 1.802 Mpa
Min Stress – 0.0009 Mpa

## Slide 12: STRAIN DIAGRAM
Result:
Max Strain – 0.033 Mpa
Min Strain– 3.447 e-6 Mpa

## Slide 13: CALCULATIONS

## Slide 14: BUOYANCY CALCULATIONS
Mass = 5.55 kg, Volume = 4.6x e^06 mm3, Density = 1025 kg/m3 (sea water)
Gravity = 9.81 m/sec2
Flow speed of the water = 1500 m/sec (Apx)
Dynamic Viscosity = 25degree Celsius (0.0089 kg/m2sec)
Formula,
  Fb = Vs × D × g, Fb - buoyancy force, Vs - submerged volume, D – density, g – gravity.
  Fb = 46.45 N
  Weight = mass x g W= 54.38N
  Weight > Buoyancy Force, Drum will submerged into the water

## Slide 15: HYDRODYNAMIC CALCULATIONS:
Reynolds Number Calculation
Rn=(ρVL)/μ
Ρ = 1200kg/m3 V = 1500 m/sec L = 0.96 m μ = 8.90 x 10^-4 kg/msec2
Rn = 1.942 x 10 ^9
Rn > 4000, so the flow is Turbulent ( Sea water flow will be turbulent)
F = m x a = 5545.65 kg x 9.81
  = 54.446 N
  Torque, T = F x r x sin(ᴓ)
  = 5.187 Nm

## Slide 16: RESULT
For the new design we have achieved
  Object will submerged into the fluid with Fb = 46.45N
  Displaced fluid 4.737 Kg
  Testing Strips – 18
  Sea water flow will be turbulent

## Slide 17: EXISTING PROBLEMS & RECOMMENDATIONS

## Slide 18: PROBLEMS
Inner View
Corrosion of
Nuts and Bolts
Assembly View
Outer View Weight Increases
Gap between
Top and Bottom Part

## Slide 19: SUGGESTING SOLUTION
Extrude cut in the Top Part
Extension in the Bottom Part
Assembling view

## Slide 20: PLASTIC NUTS AND BOLTS
  Nylon 6.6 (Polyamide 6.6) Hex Head Fully Threaded Set Screws/Bolts
  Plastic Hex Head Bolts and Screws are the ideal fasteners for mechanically securing materials
  lightweight and resistant to corrosion, oil, abrasion and most chemicals
Plastic Nuts and Bolts

## Slide 21: CALCULATIONS
Mass = 4.62x e^03 g
Volume = 3.85x e^06 mm3
Density = 1025 kg/m3 (sea water)
Gravity = 9.81 m/sec2
Formula,
  Fb = Vs × D × g, Fb - buoyancy force, Vs - submerged volume, D – density, g – gravity.
  Fb = 38.7N
  Weight = mass x g W= 45.32N
  Weight > Buoyancy force, Drum will submerged into the water

## Slide 22: MATERIAL PROPERTIES
Chemical properties:
  Effects of acids: Acrylic fibres are resistant to acids
  Effect of Alkalis: Crystalline nature prevents the entre of the alkaline
Applications:
  Transparency and high break Resistance
  Easy to fabricate
  Max Temp of Acrylic material is 80 C

## Slide 23: APPLICATION
HYDRODYNAMIC PROPERTIES
Flow : Turbulent
Torque generated : 5.187 Nm
Properties | Existing Design | New Design
Weight | 34.138N | 54.234N
Volume | 2.9 x e^6 mm3 | 4.6x e^06 mm3
Buoyancy | 29.15 N | 46.45 N
Displacement of Fluid | 2.97 kg | 4.737 Kg
BUOYANCY PROPERTIES

## Slide 24: BIO FOULING

## Slide 25: BIOFOULING
Reasons :
Expose of Micro organisms
Control of Biofouling:
  Coatings using biocides, thermal treatments, or pulses of energy.
  Thin Film in the ship Hull.
  In industrial processes, bio-dispersants are used to control underwater hull corrosion.

## Slide 27: CONCLUSION
Objectives achieved:
  New Thread locking system
  Higher Buoyance than existing design
  Testing space increased
  Recommendations:
  Further analysis on underwater testing – keeping drum below 15m
  Increase in Hollow space inside the drum
  Increasing motor HP

## Slide 28
Thank you !

## Slide 29
Questions?